## Slide 1: Introduction to Energy
Lesson Slides

## Slide 2: The production and use of energy
Lesson 1

## Slide 3: Energy flows
Electricity
(e.g. lights, appliances)
Heat
(e.g. heating homes, industrial processes)
Transport
(e.g. cars, boats, planes)
Finite resources
(e.g. coal, natural gas)
Renewable resources
(e.g. wind, sun)
Power stations
Extraction and refining
Identify which boxes the following activities sit: Production of natural gas; Burning gas for cooking; Gas occurring in undersea rock formations
Energy Supply
Energy Transformation
Energy Demand

## Slide 4: Energy flows
Electricity
Heat
Transport
Finite resources
(e.g. coal, natural gas)
Renewable resources
(e.g. wind, sun)
Power stations
Extraction and refining
Energy Supply
Energy Transformation
Energy Demand
Production of natural gas
Burning gas for cooking
Gas in undersea rock formations

## Slide 5: Energy flows
Electricity
Heat
Transport
Finite resources
(e.g. coal, natural gas)
Renewable resources
(e.g. wind, sun)
Power stations
Extraction and refining
Energy Supply
Energy Transformation
Energy Demand
Production of natural gas
Burning gas for cooking
Gas in undersea rock formations
Oil reserves
Production of jet fuel
Passenger flight
Wind
Offshore wind farm
Boiling water in kettle

## Slide 6: UK energy flows
Energy Supply
Oil, natural gas, nuclear, coal and renewable sources (e.g. wind) are the main inputs to the energy mix;
There resources are produced within the UK (indigenous) and imported from around the world;
Energy Demand
Energy is used in:
  the production of heat (e.g. gas for heating homes),
  transport (petrol or diesel in cars); and
  the generation of electricity in power stations;
Electricity and heat use can be split into domestic (e.g. people’s homes), industrial (e.g. factories) and commercial (e.g. supermarkets)
Energy is lost in the transformation of energy from one type to another and the transmission of energy from one place to another;
Some energy produced in the UK is exported – e.g. natural gas transported to Continental Europe and electricity to the island of Ireland through interconnectors;
Energy Supply
Energy Demand
Transformation
Source: Digest of UK Energy Statistics (2016), Climate Cloud

## Slide 7: Types of electricity generation
Generator – converts kinetic energy to electrical energy
Combustion to create steam in a boiler
Conversion of kinetic energy of a fluid (air / water) by a turbine (e.g. wind turbine / hydro turbine)
Electricity
Gas
Coal
Biomass
Steam turbine
Wind
Hydro
Wave / tidal
Nuclear
Radioactive heat
Steam turbine
Oil
Biogas
1
2
3
Combustion in a reciprocating engine (like a car engine)
4
Solar
Conversion of light energy to electrical energy in solar panels
5
Thermal
Input
Conversion
Output

## Slide 8: Finite vs. renewable energy
Non-finite energy sources
Finite energy sources
Energy is used faster than it can be produced naturally
Energy is used at the same rate it is produced
Production
Example
Energy types
Natural gas, coal, oil
Wind, solar, geothermal, tidal, nuclear
Coal is produced over millions of years through organic material accumulating in shallow lakes and seas. Over time, heat and pressure is applied, transforming this organic material into coal.
Coal can be mined and combusted for energy generation earth much faster than it is replenished through these natural processes. This means that, over time, the resource will be depleted.
Wind energy uses turbines that transform the kinetic energy of the wind into electrical energy. Much like the wings of a plane, wind turbine blades use passing wind to generate motion that turns the blades, which creates electricity in a generator.
Electricity is generated at the same time the wind kinetic energy resource is available, and does not therefore run out.

## Slide 9: UK electricity supply (2016)
Source: Digest of UK Energy Statistics (2017)
Available at: https://www.gov.uk/government/statistics/digest-of-uk-energy-statistics-dukes-2017-main-report

## Slide 10: The UK electricity mix has changed significantly
Percentage of generation (%)
Year
What has changed?
Increase in renewables, promoted by government schemes to support renewable electricity and advances in technology;
Decreases in coal as plants reach the end of their lives and government policies making coal generation more expensive;
Increase in generation from gas;
What drivers may have contributed to the changes shown in the chart?

## Slide 11: Energy Diary
Time | Activity | Type of energy use | Source of energy
07:00 | Breakfast | Electrical energy (microwave, kettle) | Electricity on the grid
07:45 / 16:00 | Travel to and from school | Chemical energy (petrol) | Petrol produced from oil
09:00 – 15:30 | School | Electrical energy for lights Heat energy to heat classrooms Electrical energy for computers | Electricity on the grid Gas from grid
12:30 | Lunch | Energy to produce foods: Energy to produce food – fertiliser, feed for animals etc.; Energy to transport food from source to plate; Heat energy to cook food; | Petrol produced from oil for Transport Gas for heating food
19:00 | Watch TV | Electrical energy for TV | Electricity from the grid
19:30 | Dinner | Electrical energy to produce heat for cooking | Electricity from grid
What is your energy diary for yesterday? Think through where you have used energy by consuming electricity, in heating and transport. Given the UK energy mix, where is this likely to have come from?

## Slide 12: Reducing energy demand
How can you reduce your energy consumption? What are the costs and benefits associated with each?
Electricity
Heat
Transport
Use less by changing what you do
Use less by using energy more efficiently
Switch off appliances on standby;
Charging phones only for time required;
Switch off lights you don’t need;
Replace lights with LED bulbs;
Upgrade old appliances (fridge, washing machine)
Turn heating down by 1 degree;
Turn heating off in rooms that aren’t used;
Switch from oil to gas;
Home insulation;
Upgrade old gas boilers;
Cycle
Mass transit – bus / train / tram
Electric vehicles
Efficient driving;
Upgrade car to a smaller car / smaller engine;

## Slide 13: Types of Renewable Energy
Lesson 2

## Slide 14: UK Electricity Generation Mix (2016)
Source: Digest of UK Energy Statistics (2017)
Available at: https://www.gov.uk/government/statistics/digest-of-uk-energy-statistics-dukes-2017-main-report
Types of renewable technology

## Slide 15: Renewable technologies
Wind
Solar
Hydro
Tidal
Geothermal
Energy source
Kinetic energy of the wind
Heat and light energy from the sun
Kinetic energy of water in rivers
Kinetic energy of tides
Heat energy from the ground / air
Biomass
Energy stored in organic material
Technologies
Wind turbines (onshore / offshore)
Solar PV
Solar thermal
Concentrated solar power
Run-of-river
Dams
Tidal lagoons
Underwater turbines
Deep geothermal
Air source heat
Ground source heat
Biomass combustion
Anaerobic digestion
Biofuels
Landfill gas
Energy use
Electricity
Electrticity / heat
Electricity
Electricity
Heat / Electricity
Heat, transport, electricity
What resources does the UK or your local geography have that might be used to generate renewable electricity?
Pick a renewable technology and describe what environmental conditions would best suit the technology. Consider the process of building and operating the applicable technology.

## Slide 16: Types of electricity generation
Generator – converts kinetic energy to electrical energy
Combustion to create steam in a boiler
Conversion of kinetic energy of a fluid (air / water) by a turbine (e.g. wind turbine / hydro turbine)
Electricity
Gas
Coal
Biomass
Steam turbine
Wind
Hydro
Wave / tidal
Nuclear
Radioactive heat
Steam turbine
Oil
Biogas
1
2
3
Combustion in a reciprocating engine (like a car engine)
4
Solar
Conversion of light energy to electrical energy in solar panels
5
Thermal
Input
Conversion
Output

## Slide 17: Case Study: UK Offshore Wind (1)
Offshore wind was responsible for c. 5% of the UK electricity generation mix in 2016;
Due to the UK’s shallow continental shelf and regular, predictable wind speeds, it is likely to be an increasingly important contributor to UK electricity;
Wind speeds are higher and more predictable offshore than onshore;
Less public opposition as offshore wind developments have less visual and noise impacts compared with onshore wind projects;
Higher costs to develop and operate offshore projects due to the complexities of installing turbines offshore.
UK is the world leader in offshore wind, with more capacity installed than any other country.
UK offshore wind projects in operations (green) or development (purple). Source: The Crown Estate

## Slide 18: Case Study: UK Offshore Wind (2)
Key Components of an Offshore Wind Farm
Wind turbine generators (“WTGs”);
Foundations;
Array cables (network between WTGs);
Export cables (transmit electricity from offshore to onshore);
Substations
Research online to find an example of a UK based offshore wind farm.
Summarise the key characteristic of the project.

## Slide 19: Case Study: UK Offshore Wind (3)
Gemini wind farm, Netherlands

## Slide 20: Case Study: Geothermal
Krafla Geothermal Plant, Iceland, Europe
The Krafla Geothermal Plant is located near Myvatn, Iceland. The power station commenced development in 1977, with regular operations starting the following year. The plant has 18 boreholes, through which water is pumped into the earth’s surface to a depth of up to 2.2 km. The water is heated by the naturally occurring hot rocks, where it is turned to steam and returns to the surface at pressure.
The steam is transported by overground pipes (see picture above) to two 30 MW steam turbines, where the heat and pressure is converted to electricity.
The project is located in a highly volcanic area of Iceland, at the location the Mid-Atlantic Ocean ridge meets land. At this location, the European and American tectonic plates are moving apart. The last period of volcanic activity was in 1977, as part of an eruption called the Krafla fires.
Iceland

## Slide 21: Energy challenges
Lesson 3

## Slide 22: The Energy ‘Trilema’
Security of supply
Meeting energy demand to ensure there are no ‘black-outs’
Reliance on other states to supply energy through imports
Green Agenda
Demands to reduce the production of greenhouse gases to avoid environmental impacts
Cost of energy
Minimising the cost of energy for consumers and businesses
Energy Policy needs to balance three elements

## Slide 23: What drives energy cost (1)?
The cost of energy is a function of its generation and transport
Cost of Energy
££££
Generation
Transport
Upfront costs
How much does it cost to build or discover the energy generation?
Ongoing costs
How much does it cost to operate and maintain the energy generation?
Input costs
What inputs are required (e.g. fuels such as coal) and how much does this cost?
End of life costs
What happens when the resource can no longer generate?
Distance
How far away is the energy supply from the energy demand?
Losses
What energy is lost in transportation?

## Slide 24: What drives energy cost (2)?
The below table shows different sources of energy and whether the cost of generating and transporting that energy is high / medium or low. Discuss and explain the factors resulting in the cost profile for each.
Electricity (nuclear)
Electricity (gas)
Electricity (offshore wind)
Transport (electric car)
Transport (petrol car)
Heat (burning oil)
Upfront costs
End of life costs
Ongoing costs
Input costs
Generation
Distance
Losses
Transport
Reasons / Explanation
High cost
Medium cost
Low cost

## Slide 25: What drives energy cost (3)?
Electricity (nuclear)
Electricity (gas)
Electricity (offshore wind)
Transport (electric car)
Transport (petrol car)
Heat (burning oil)
Upfront costs
End of life costs
Ongoing costs
Input costs
Generation
Distance
Losses
Transport
Reasons / Explanation
High cost
Medium cost
Low cost
Large projects with high upfront and decommissioning costs. Plentiful fuel.
Established technology. Fuel costs based on gas price
New technology and complex offshore build / end of life. Wind is free.
Established product, widely available. Petrol costs high.
New product early in life. Relies on centrally generated power for recharge
Widely available efficient technology. High costs to buy and deliver oil
The below table shows different sources of energy and whether the cost of generating and transporting that energy is high / medium or low. Discuss and explain the factors resulting in the cost profile.

## Slide 26: Security of supply
Ensuring energy supply meets demand: ‘Keeping the Lights on’
Energy Supply
Energy Demand
Population growth
Economic growth
Energy efficiency
Technological change
Weather
Global competition for resource
Politics of energy
Fuel costs
Technology mix
Available reserves / new discoveries
Discuss the links between politics and energy.
Think about:
Why do politicians care about ensuring supply meets demand? How critical is energy to society?
Are energy resources equally distributed around the globe?
What are the risks of political instability on the supply of energy?

## Slide 27: Green agenda
Wind
Solar
Hydro
Tidal
Geothermal
Biomass
Benefits
Challenges
Plentiful resources – UK has some of the best wind resources in the world, in particular offshore due to shallow waters and high wind speeds;
Lower capital and operating costs compared with other renewables, with costs reducing significantly as more capacity is deployed;
Very predictible and can meet ‘baseload’ requirements (i.e. generates all the time);
Predictible (based on the timing of tides);
UK has good tidal resources;
Predictible, baseload energy supply.
Predictible, baseload supply;
Can use existing coal plants (co-firing / conversion), reducing the need for new infrastructure;
Intermittent supply that is hard to predict;
High capital costs (costs to build);
Visual impacts on the landscape;
Intermittent, but more predictible than wind;
Limited UK resource, with solar being more feasible in the South compared with the North of the country;
Environmental issues of diverting or damming rivers – river biodiversity
Environmenta impacts of large new lakes
High capital costs to install and ongoing costs to operate and maintain
Environmental issues with building tidal lagoons – fish and bird life
High cost to build in the UK, limited resources due to geology;
Limited heat networks to transport heat to end users
Sustainability issues – ensuring the biomass is produced in a sustainable way;
Energy crops – impacts on food availability / prices where agriculture shifts to energy production from food.
Renewable technologies have advantages and disadvantages

## Slide 28: Energy policy examples
Security of supply
Green Agenda
Cost of energy
Energy Policy needs to balance three elements
Subsidies for renewable technologies to enable them to compete with conventional generation;
Additional taxes or costs on fossil fuelled generators (e.g. carbon emissions tax);
Changing building regulations for new homes, requiring more energy efficient homes;
Support for electric vehicles – e.g. building a charging network
Transport sharing / additional public transport
Subsidise energy costs, in particular for those least able to pay;
Price caps / regulated pricing;
Promotion of smart meters, providing information relating to energy use and cost;
Promotion of national infrastructure to reduce reliance on foreign geographies;
Diversification of energy sources, to ensure there is no reliance on a single technology (e.g. nuclear);
Can you think of any other policies governments may use to support any aspect of the trilema?

## Slide 29: Energy policy exercise
The table below shows a number of energy policies. By re-creating this table, comment on each against the three aspects of the energy trilema.
Policy
Security of supply
Green agenda
Cost of energy
The introduction of subsidies for renewable energy
Development of new electricity interconnectors with Europe
Development of new nuclear power stations
Implementation of a gas supply price cap for residential customers

## Slide 30: Energy policy exercise (2)
The table below shows a number of energy policies. By re-creating this table, comment on each against the three aspects of the energy trilema.
Policy
Security of supply
Green agenda
Cost of energy
The introduction of subsidies for renewable energy
Development of new electricity interconnectors with Europe
Development of new nuclear power stations
Implementation of a gas supply price cap for residential customers
Solar and wind are intermittent and therefore unpredictable.
Subsidies promote the deployment of renewable generation
Subsidies increase the cost of energy as the cost of the subsidy is passed to end users
Nuclear power is highly predictable and constant
Emissions from the operations of a nuclear plant are low
High cost of energy as a result of high upfront costs associated with construction
Unlikely to have an impact on security of supply
Unlikely to have an impact on green agenda
Capping energy prices limits the costs consumers pay
More interconnection increases the potential sources of supply and therefore enhances security
Dependent of the make-up of energy at the source
Interconnectors are expensive to build and the costs of the energy is dependent on the cost of energy at the origin